## Slide 1
Models：
Feature:
◆1st led is the battery type setting
◆2ndled is for charging frequency
◆3rd led is for charging priority, only set the percentage
◆you want for battery #1, the controller will automatically calculate the rest for battery #2.
www.szgoland.com www.szgoland.net
Type | Current | Volts
EPIP20-2 | 10A | 12/24V auto work
EPIP20-2B | 20A | 12/24V auto work
EPIPDB series adopts dual battery design and Various types of batteries supported.A single battery can work -the other one battery can be charge.It can use Sealed battery,Gel battery,Flooded battery.
PWM Solar charge controller
with dual battery
EPIPDB SERIES

## Slide 2
Charging priority:
Number | Battery#1 | Battery#2
shows | charging | charging
0 | 0% | 100%
1 | 10% | 90%
2 | 20% | 80%
3 | 30% | 70%
4 | 40% | 60%
5 | 50% | 50%
6 | 60% | 40%
7 | 70% | 30%
8 | 80% | 20%
9 | 90% | 10%
www.szgoland.com www.szgoland.net
Note:in the normal charging status ,the controller will divide the charging as the setting.While battery #1 is fully charger,more charge current will be diverted to battery #2.amd return to the setting charging automatically when the battery#1 is in low voltage.When the controller detects there is only #1,all the charging will go to the battery #1 automatically.

## Slide 3
Setpoint | Sealed battery | Floodedbattery | Gel battery
Regulation voltage | 12.2V | 14.4V | 14.6V
Boost voltage | 14.4V | 14.6V | 14.8V
Float voltage | 13.7V | 13.7V | 13.7V
Maximum solar voltage | 30V(or 55V) |  | 
Battery voltage range | 1-15V |  | 
Boost time | 30 minutes |  | 
Self-consumption | 4mA at night, 10mA at charging |  | 
Meterbus connectio | 8-pin RJ-45 |  | 
Temp. compensation | -30mV/12V |  | 
Terminals | 4mm2 |  | 
Temperature | 35℃ to +55℃ |  | 
TECHNICAL INFORMATION:
Goland Century CO.,LTD.
Add: Room 608, Xintun Building, No.50, Xintun Middle Road, Longgang District, Shenzhen, Guangdong
Tel:86-755-26827243
Fax: 86-755-26805950
E-mail: info@szgoland.net/info@szgoland.com
Website:www.szgoland.net
www.szgoland.com www.szgoland.net